## Slide 1: DeepPlankter
Block Diagram

## Slide 2
Controller/Navigator
ESC
Motor
Servo
Rudder
Solar panels
MPPT
Solar panels
MPPT
Battery 1
Battery 2
GPS/eCompass
Iridium
Camara Module
LoRa
4G
Weather Station
Water Station
Deck
Bottom
Hull
R/C
Servo
Rudder

## Slide 3
Controller/Navigator
MCU
UART x 7
BAT I/V Sens
BAT I/V Sens
IMU
Pressure Temperature
Humidity
ESC
Servo
SPI x 2
I2C x 2
SBUS/PPM
Cam
SDCard

## Slide 4
Controller/Navigator
BAT0
BAT1
ESC
SERVO1
SERVO2
5V x 3
VBAT x 3
3.3V x 4

## Slide 5: Water station
Temperature, PH, TDS, Turbidity sensor

## Slide 6: Weather Station
Wind
  Direction
  Speed
Pressure
Temperature
Humidity
RGB
Ambient light
  MAX44009

## Slide 7
Telemetry 1
(UART3)
Telemetry 2
(UART5)
AUX UART2
(UART8)
(I2C4)
(I2C4)
GPS
(UART9)
AUX UART1
(UART7)
AUX SPI1
(SPI4)
AUX SPI2
(SPI4)
TELE1/2 and GPS have 2 extra pins for flow control and power control. AUX UART1/2 have no extra pins.
TELE1 (UART3) -> LORA
TELE2 (UART5) -> Iridium
AUX UART2 (UART8), 5V CH1 -> SIM800c.
GPS (UART9) -> GPS AR68GB

## Slide 8: Iridium SBD9602 Connector
5V | GND | RX (input) | SGND | DSR | RI | DTR | RES | SGND | 3.3v LED
5V | GND | ON/OFF | TX (output) | DCD | CTS | RTS | SGND | RES | Network Available
1
2
20
DTR must be low for the module to receive AT CMD